TEMPLATING FACT SHEET,

PLEASE PASS THIS ON TO YOUR KITCHEN INSTALLER

To enable us to complete your template satisfactorily, please be aware of the following points:

PLEASE NOTE THE MAJORITY OF OUR TEMPLATES ARE COMPLETED DIGITALLY. THIS REQUIRES A COMPLETELY EMPTY KITCHEN FOR AT LEAST 2 HOURS. ALL TEMPORARY TOPS TO BE REMOVED AND ALL OTHER ITEMS COMPLETELY CLEARED FROM THE AREA.

All base units must be firmly fixed to the walls and levelled.

DAY OF TEMPLATING: Landford Stone will be using digital technology when we come out to template your new kitchens and bathrooms etc. To help us with a smooth fast process, we would like to ask that on the date of the template, the kitchen is kept clear and all builders/contractors can vacate the room until templating is completed.

SINKS/BOWLS: All under mounted, ceramic or cast iron sinks must be supported in the base unit on a framework/cradle. Stainless Steel sinks preferably mounted as above but these can be suspended from the granite if necessary. Stainless Steel sinks MUST be mounted in a cradle for engineered stone worktops. Please note that we do not suspend bowls from 20mm or 20+20mm granite. All sinks MUST be on site when the templater arrives.

TAPS/DRINKING WATER FILTER & POP UP SOCKETS: All taps and electrical pop up sockets should be on site when the templater arrives. If this is not possible all relevant information should be available to the Templater i.e. Hole size and tap throw. All tap positions to be marked out on units or walls prior to the templater arriving

HOBS, AGA & RANGE COOKERS: All hobs MUST be on site when the templater arrives. Unless your AGA/Rayburn etc. is fitted in the final position we cannot template to an acceptable standard and therefore no work can be undertaken until this is achieved. This includes all Aga’s and Range cookers.

BREAKFAST BARS, ISLANDS & PENISULARS: All units should be fixed and screwed together to give a solid and stable base on which the worktop is to be installed, there should be little or no movement of the cabinets and all panels and end panels should be securely fixed and in their final place. For 20+20 thick worktops, an 18mm MDF or plywood sub base should be fitted to the top of the units for the underside of the worktop to sit on. This base can be 100 mm smaller than the final granite’s underside dimensions. This is to avoid larger unsupported areas of material with only the outside double edge sat on the units. The maximum unsupported overhang recommended is 300mm for breakfast bar areas. Bigger overhangs will need further support to be installed such as legs, brackets or corbel supports. With certain more fragile materials, and thinner sintered materials, a ‘solid top’ may well need fitting within the cabinets to sit flush with the unit top… this is to avoid unsupported material sagging where it is not resting on the unit carcasses.

TILING: Any existing tiling may need to be removed prior to installing your worktops ( the templator will advise you). Any new tiling should be carried out after the worktops have been installed.

20+20 OR 30+30 WORKTOPS: Templaters will discuss and advise the customers what will be required prior to installation.

REPLACEMENT TOPS: Please arrange for all existing worktops to be removed by a carpenter/kitchen fitter prior to the Templater’s arrival. This includes the removal of sinks, taps and hobs. The units will need to be checked thoroughly that they are solid and stable for new worktops.

WORK REQUIRED PRIOR TO INSTALLATION: The templater will advise you of any work that you will be required to do such as battening after his templating visit. Should this work not be carried out prior to installation, this could cause a delay in fitting.

If our Templater cannot complete the template due to problems on site, it will probably necessitate an additional visit, which may incur delay and extra costs. If you have any technical questions regarding the above, please do not hesitate to call and ask for a Technical Adviser or a Templater.

PLEASE NOTE THAT LANDFORD STONE WILL NOT BE ABLE TO DISCONNECT/CONNECT ANY ELECTRICAL APPLIANCES, PLUMBING OR GAS AS OUR MEN ARE NOT CERTIFITED TO DO SO.

Whilst every care will be taken, accidental damage will not be the responsibility of Landford Stone. Stone is an extremely heavy material; please ensure that you protect all appliances, doors, units etc.

April 2016